## Slide 1: Instruction Pipelining and Hazards
The Preston M. Green Department of Electrical and Systems Engineering
An Zou
anzou@wustl.edu
Notes: 各位同学大家好，今天我将给大家讲解计算机体系结构中最重要的概念之一：指令流水线和指令流水线中的冒险
在组合逻辑电路中，不同路径的输入信号变化传输到同一点门级电路时，在时间上有先有后，这种先后所形成的时间差称为竞争（Competition）
由于竞争的存在，输出信号需要经过一段时间才能达到期望状态，过渡时间内可能产生瞬间的错误输出，例如尖峰脉冲。这种现象被称为冒险（Hazard）

## Slide 2: Single Instruction Execution
Instruction execution from C to assembly code
  ­­Assembly code for a = b+c:
  lw Rb, b
  lw Rc, c
  add Ra, Rb, Rc
  sw Ra, a
Load b to register Rb
Load c to register Rc
Add the value in register Rb and Rc to register Ra
  C code for a = b+c:
  int a = b + c;
write register Ra to memory a
Notes: 我们先从一个简单的例子开始
我们可以简单的写一句C语言的指令来实现整型数的加法运算。例如整型数b和c相加，结果给a。
为了执行这个语句，编译器首先这个语句编译成汇编代码，之后再翻译成机器码在处理器上执行。
在此我们可以简单的理解为机器码是汇编码的翻译。汇编代码就是实际在处理器上执行的语句。
为了执行上面这句b+c赋值给a的语句，一共需要4条汇编指令，
即将b的值从内存中拷贝到处理器的寄存器Rb中
将c的值从内存中拷贝到处理器的寄存器Rc中
将处理器Rb和Rc的值相加，并将结果放在寄存器Ra中的值写回到内存中
最后将寄存器Ra中的值写回到内存中

## Slide 3: Single Instruction Execution
Assembly execution on the digital circuit
Instruction fetch
Reg access / decode
ALU operation
Data access
Reg
write-
back
  add Ra, Rb, Rc
Notes: 之后，处理器通常需要五个步骤和硬件电路去执行上面的每一条指令。
我们以”将Rb和Rc的值相加，并将结果放在寄存器Ra中” 这条指令为例
首先是取指令，即将上面这条指令从内存中读入到处理器中
第二步是读取处理器中的值，并对指令进行译码，例如在上面这个指令中就是对指令进行译码，知道是进行加法运算，同时去寄存器Rb和Rc中将数据取出来
第三步是进行数值运算即计算Ra和Rb相加的结果
第四步是内存访问，这条指令不需要进行内存访问。这条指令不需要内存访问。向其他的一些指令，如之前的去内存中读取数值或者向内存中写入数值，都需要执行这一步。
第五步就是将计算结果写入到寄存器中，在这条指令里面就是写入到寄存器Ra中
Then, the machine code needs these steps to execute on hardware digital circuit. Let us the machine code add he value in register Rb and Rc to register Ra as example. First, the digital circuit need to fetch this instruction for cache or memory. Then the digital circuit needs to decode the instruction to know what operation it is and also access the registers used in this instruction. Next, it needs to do the calculation operation here it is addition. In other instructions such as memory read and write, the calculation operation calculate the target address. After this, it will access cache or memory if needed. Final, the value is written to the target register. In this example, it is register Ra.

## Slide 4: Single Instruction Execution
Problems
Instruction fetch
Reg access / decode
ALU operation
Data access
Reg
write-
back
  Wasted resource and low instruction execution speed
Notes: 通过这个例子，我们可以发现，上面介绍的执行方法好像效率有点低。比如说当指令在译码阶段，只有这部分硬件电路在工作，其他的硬件电路都处在闲置状态。同样，当这条指令读取处理器中的值，并对指令进行译码时，其他的硬件电路也处在闲置状态。不难发现，这种执行方法对硬件资源的利用率很低，同时当硬件电路都处在闲置状态也会有相应的能耗。
With this example, we can notice the inefficiency in this instruction execution. When the instruction are in the instruction fetch status, only this part of digital circuits are used. Similarly, when the instruction comes to the decode and register access stage, other digital circuits are in idle. This execution manner has a low resource utilization rate. Meanwhile, when the digital circuits are in idle, they are still consuming power.

## Slide 5: Single Instruction Execution
Multiple Instruction Execution Order
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  lw Rb, b
  lw Rc, c
Cycle 8
Cycle 9
Notes: 同时，如果有多个指令依次执行，我们用这些符号来代表上面每一个执行步骤
比如说我们之前介绍的指令
先将b的值从内存中拷贝到处理器的寄存器Rb中
再将c的值从内存中拷贝到处理器的寄存器Rc中
第二个语句只有当第一个语句执行完之后才能执行
这意味着每个指令的延迟很长，并且这个处理器的语句执行速率很慢，性能很低
When multiple instructions are execution in this manner, the next instruction can start only after the previous instruction finish. Therefore, each instruction has a long latency and the system has a slow instruction execution speed, which means a low performance.

## Slide 6: Pipelined Instruction Execution
The idea of pipelining (laundry example)
Step 1
Step 2
Step 3
Step 4
Step 6
Step 7
Step 5
Step 8
Step 9
Notes: 为了提高指令的执行效率，流水线的思想被引入进来。让我用个简单的例子来介绍流水线。我们假设我们在家里洗衣服，有好多筐衣服要洗。洗衣服有3个步骤，第一步是是洗衣机洗衣服，第二步是烘干机对洗好的衣服进行烘干，第三步是把衣服叠好收起来。
实际上，当我们开始洗第一筐衣服的时候，我们并不需要等上面三步都完成再去洗第二筐。我们可以在第一筐衣服在洗衣机里洗完去烘干的时候，开始洗第二筐衣服。同样，在第二筐衣服在洗衣机里洗完去烘干的时候，开始洗第三筐衣服。这样可以大大提升我们洗衣服的效率。
To increase the instruction execution speed, pipelined execution are introduced. Let us use a simple example to show how the pipeline works. We assume that we are doing laundry at home. It has three steps. First washing with wash machine. Second is drying with dryer. The third step is folding the clothes. After we wash the first basket of clothes, we do not need to wait all these three steps to finish and then start the second basket. We can start the second basket when the washer is free and comes to the dryer. Similarly, the second basket can start when the second basket finish the first step. So on and So forth.

## Slide 7: Pipelined Instruction Execution
Pipelined Execution
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  lw Rb, b
  lw Rc, c
  add Ra, Rb, Rc
  sw Ra, a
Notes: 我们回到之前的指令执行的问题，如果我们可以把同样的流水线的方法方法用在指令执行的过程中，也可以大大提高指令执行的效率。第二条指令可以在第一条指令完成第一步的时候就开始执行。同样，第三条指令可以在第二条指令完成第一步的时候就开始执行。
Then we come back to our instruction execution problem. The second instruction can execute when the first instruction finishes its first stage which is instruction fetch. The third instruction can execute when the second instruction finishes its first stage which is instruction fetch. So on and so forth. When there are N instructions, it will take N+4 cycles to finish all the instructions. When the number of instruction is large enough, the average instruction execution rate is 1 instruction per cycle.

## Slide 8: Pipelined Instruction Execution
Pipelined Execution
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
N条指令
5N个周期
N条指令
N+4个周期
Notes: 假设一共有N条指令，每个指令需要5个周期T的完成
那么之前的方法需要5NT个周期来完成
如果当指令的数量足够多，我们可以发现，执行这些指令的时间缩短了5倍，执行效率提高了5倍

## Slide 9: Pipelined Instruction Execution
Pipelined Execution
The good news
  Multiple instructions are being processed
  at same time。
  Best case speedup of stage number.
The bad news
  Instructions interfere with each other - hazards
    Example: different instructions may need the same piece of hardware (e.g., memory) in same clock cycle
    Example: instruction may require a result produced by an earlier instruction that is not yet complete
    Example: instructions are not in order because of branches
Notes: 目前我们介绍了指令流水线的基本思想和概念。指令流水线的核心思想便是利用不同资源的指令同时执行，这样可以提高指令执行效率。当指令的数量足够多，最好的情况下可以提升流水线级数倍的效率。
然后，简单的流水线也引入了一些问题，例如指令之间的相互影响。
例如如果多个指令需要在同一时间利用或者访问同一块硬件资源怎么办
例如下一条指令需要的结果上一条指令还没有来得及放到对应的寄存器中
又或者是出现了if这种判断跳转指令怎么办？
上面这些问题都可以归结为流水线中的冒险问题。

## Slide 10: Pipeline Hazards
Hazards
  Structural hazards:
  Two different instructions use same hardware in same cycle
  Data hazards:
  Instruction depends on result of prior instruction still in the pipeline
  Read after write (RAW): a true dependency.
  Write after read (WAR): an anti-dependency (no hazards).
  Write after write (WAW): an output dependency (no problem in atom execution and problems in concurrency).
  Control hazards:
  Pipelining of branches & other instructions that change the PC
Notes: 流水线中的冒险主要可以归结为3类
结构冒险（Structural Hazard）、
数据冒险（Data Hazard）
以及控制冒险（Control Hazard）
结构冒险同一时间利用或者访问同一块硬件资源
数据冒险指的是下一条指令需要上一条指令的计算结果
控制冒险便是当出现了跳转指令时，流水线在不知道跳转的计算结果的时候，该执行哪一条语句的问题。
下面我们将依次介绍这几种冒险，并给出他们对应的解决办法

## Slide 11: Pipeline Hazards
Hazards
  Structural hazards:
  Two different instructions use same hardware in same cycle
  Data hazards:
  Instruction depends on result of prior instruction still in the pipeline
  Read after write (RAW): a true dependency.
  Write after read (WAR): an anti-dependency (no hazards).
  Write after write (WAW): an output dependency (no problem in atom execution and problems in concurrency).
  Control hazards:
  Pipelining of branches & other instructions that change the PC
Notes: 首先我们来看结构冒险（Structural Hazard）

## Slide 12: Pipeline Hazards
Structural Hazards：
  Two different instructions use same hardware in same cycle
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
C
C
If there is one memory (cache) for both data and instruction
Memory
Notes:   在第 1 条指令执行到访存（MEM）阶段的时候，流水线里的第 4 条指令，在执行取指令（Fetch）的操作。访存和取指令，都要进行内存数据的读取。我们的内存，只有一个地址译码器的作为地址输入，那就只能在一个时钟周期里面读取一条数据，没办法同时执行第 1 条指令的读取内存数据和第 4 条指令的读取指令代码。
  类似的资源冲突，其实你在日常使用计算机的时候也会遇到。最常见的就是薄膜键盘的“锁键”问题。常用的最廉价的薄膜键盘，并不是每一个按键的背后都有一根独立的线路，而是多个键共用一个线路。如果我们在同一时间，按下两个共用一个线路的按键，这两个按键的信号就没办法都传输出去。
  这种情况便被称为结构冒险

## Slide 13: Pipeline Hazards
Hazards
  Structural hazards:
  Two different instructions use same hardware in same cycle.
  Data hazards:
  Instruction depends on result of prior instruction still in the pipeline
  Read after write (RAW): a true dependency.
  Write after read (WAR): an anti-dependency (no hazards).
  Write after write (WAW): an output dependency (no problem in atom execution and problems in concurrency).
  Control hazards:
  Pipelining of branches & other instructions that change the PC.
Notes: 第二种冒险是数据冒险
数据冒险有三种
先写后读
先读后写
写后再写

## Slide 14: Pipeline Hazards
Data Hazards：Read after Write
  Instruction depends on result of prior instruction still in the pipeline
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  add Ra, Rb, Rc
  add Re, Ra, Rd
C
C
Ra is ready after Cycle 5 but we use it at Cycle 3
Notes: 先写后读，顾名思义
上一条指令写入了寄存器，下一条指令从寄存中读入
比如说
第一条指令把寄存器Rb和Rc中的数据相加，写入到寄存器Ra中
第二条指令把寄存器Ra和Rd中的数据相加，写入到寄存器Re中
乍一看，没有问题，第一套指令先写入到寄存器Ra中，第二条指令再从Ra中读取。没有问题，是正确的数据。但是如果仔细看流水线的执行过程，我们就会发现，真正把Ra中的数据进行更新的是第五个周期。
但是第二条指令读取这个寄存器却发生在了第二个周期。
实际上读取的结果是错误的。
这个先写后读的依赖关系，我们一般被称之为数据依赖，也就是 Data Dependency
为此，这个先写后读的数据依赖存在冒险。

## Slide 15: Pipeline Hazards
Data Hazards：Write after Read
  Instruction depends on result of prior instruction still in the pipeline
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  add Rb, Ra, Rc
  add Ra, Rc, Rd
C
C
Ra is read at Cycle 2 and we update it at Cycle 6: Correct
Notes: 第二种情况是先读后写
第一条指令在第二个周期便从寄存器Ra中读取了数据，
第二条指令在第六个周期才更新寄存器Ra中的数据。
没问题，读取的是正确的，没有被更新的数据。

## Slide 16: Pipeline Hazards
Data Hazards：Write after Write
  Instruction depends on result of prior instruction still in the pipeline
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  add Ra, Rb, Rc
  add Ra, Rc, Rd
C
C
No problem for atom execution and will cause problem in concurrency (multiple instruction are executed simultaneously)
Notes: The third data hazard is called write after write. The first instruction writes register Ra at cycle 5 and the second instruction write the result to the same register Ra at cycle 6. The second writing will overwrite the first writing. This is totally correct. No problem for atom execution and will cause problem in concurrency
第三种便是先写再写。
第一条指令和第二条指令都需要像Ra中写入数据，第一条指令在第五个周期写入，第二条指令在第六个周期写入。目前来说是对的，因为第二条指令写入的数据对第一条进行了更新。
但是如果(for example, two types of multiple instruction are executed by two sets of hardware simultaneously)
这个写后再写的依赖，一般被叫作输出依赖，也就是 Output Dependency。

## Slide 17: Pipeline Hazards
Hazards
  Structural hazards:
  Two different instructions use same hardware in same cycle
  Data hazards:
  Instruction depends on result of prior instruction still in the pipeline
  Read after write (RAW): a true dependency.
  Write after read (WAR): an anti-dependency (no hazards).
  Write after write (WAW): an output dependency (no problem in atom execution and problems in concurrency).
  Control hazards:
  Pipelining of branches & other instructions that change the PC
Notes: 结构冒险（Structural Hazard）、
数据冒险（Data Hazard）
以及控制冒险（Control Hazard）

## Slide 18: Pipeline Hazards
Control Hazards：
  Pipelining of branches & other instructions that change the PC
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
beq Ra, Rb, there
there: add Ra, Rb, Rc
Branch to flag “there” if Ra is equal to Rb
C
Notes: The third type of hazard is control hazard. For example, let us take a look at a branch instruction. This instruction means Branch to flag “there” if Ra is equal to Rb. In this case, next instruction will be the fourth instruction. So that previously executed instructions are wrong. The system has to recover and start the fourth instruction.

## Slide 19: Summary
Pipelined Execution
The good news
  Multiple instructions are being processed
  at same time
  Best case speedup of N (N is stage number.)
Hazards
  Instructions interfere with each other - hazards
    Structure hazards: Example: different instructions may need the same piece of hardware (e.g., memory) in same clock cycle
    Data hazards: Example: instruction may require a result produced by an earlier instruction that is not yet complete
    Control hazards: Example: instructions are not in order because of branches
Notes: Now, let us have a brief summary of the pipeline instruction execution. For the advantages of pipelined execution, multiple instructions are being processed at same time. The pipeline can work because the stages are isolated by registers. The most significant one is the that it can speedup the instruction execution speed by N times. N is the number of stages. Every coin has two sides. Pipeline also brings extra problems. The instructions can interfere with each other which is call hazards. For example, XXX.

## Slide 20: Pipeline Hazards
Structural Hazard Solution：
  Add more resources (e.g. data memory and instruction memory)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Data Mem
Inst Mem
Notes:   解决这种问题的本质方法就是增加资源。例如，对于访问内存数据和取指令的冲突，一个直观的解决方案就是把我们的内存分成两部分，让它们各有各的地址译码器。这两部分分别是存放指令的程序内存和存放数据的数据内存。
  样把内存拆成两部分的解决方案，在计算机体系结构里叫作哈佛架构（Harvard Architecture）。对应的，我们之前说数据和指令都存在同一块内存中结构就是冯·诺依曼体系结构，又叫作普林斯顿架构（Princeton Architecture）。
  我们今天使用的 CPU，仍然是冯·诺依曼体系结构的，并没有把内存拆成程序内存和数据内存这两部分。因为如果那样拆的话，对程序指令和数据需要的内存空间，我们就没有办法根据实际的应用去动态分配了。虽然解决了资源冲突的问题，但是也失去了灵活性。
  现代的 CPU 虽然没有在内存层面进行对应的拆分，却在 CPU 内部的高速缓存部分进行了区分，把高速缓存分成了指令缓存（Instruction Cache）和数据缓存（Data Cache）两部分。

## Slide 21: Pipeline Hazards
Reg
ALU
Ifetch
Data Hazard Solutions:
  Adding pipeline stall (also called pipeline bubbling)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  add Ra, Rb, Rc
  add Re, Ra, Rd
Notes: 所以，我们需要有解决这些数据冒险的办法。其中最简单的一个办法，不过也是最笨的一个办法，就是流水线停顿（Pipeline Stall），或者叫流水线冒泡（Pipeline Bubbling）。流水线停顿的办法很容易理解。如果我们发现了后面执行的指令，会对前面执行的指令有数据层面的依赖关系，那最简单的办法就是“再等等”。我们在进行指令译码的时候，会拿到对应指令所需要访问的寄存器和内存地址。所以，在这个时候，我们能够判断出来，这个指令是否会触发数据冒险。如果会触发数据冒险，我们就可以决定，让整个流水线停顿一个或者多个周期。

## Slide 22: Pipeline Hazards
Data Hazards Solutions:
  Bypass (or forward) data directly to the consuming pipeline stage
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
  add Ra, Rb, Rc
  add Re, Ra, Rd
Notes: 在解决数据冒险问题之前不需要等待指令的执行结束。对于上述的代码序列， 一旦ALU生成了加法运算的结果，就可以将它用作减法运算的一个输入项。从内部资源中直接提前得到缺少的运算项。例如在这个问题中，ALU data generated at end of EX; consumed at beginning of EX。那么就可以在两个指令的EX阶段之间加个旁路：

## Slide 23: Pipeline Hazards
Control Hazard Solution：
  Fetch and cancel When Taken
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
beq Ra, Rb, there
there: add Ra, Rb, Rc
Notes: 意思就是假设分支不发生，让流水线按顺序往下fetch。如果后来发现真的要branch了，就清空流水线（cancel instructions），相当于插入了bubble。如果没branch就按原计划执行，无bubble

## Slide 24: Solutions to Hazards
Hazards
  Structural hazards:
  Two different instructions use same hardware in same cycle.
  S: Increase available resources, such as having multiple ports into main memory and multiple ALU (Arithmetic Logic Unit) units.
  Data hazards:
  Instruction depends on result of prior instruction still in the pipeline.
  Read after write (RAW): a true dependency.
  Write after read (WAR): an anti-dependency (no hazards).
  Write after write (WAW): an output dependency (no problem in atom execution and problems in concurrency).
  S: Insert a pipeline bubble whenever a read after write (RAW) dependency is encountered; bypassing and so on.
  Control hazards:
  Pipelining of branches & other instructions that change the PC.
  Branch prediction: guess the outcome of a conditional operation and execute the most likely result.
Notes: 结构冒险（Structural Hazard）、
数据冒险（Data Hazard）
以及控制冒险（Control Hazard）